5 Quick & Easy RFI Solutions
Bob Brehm, AK6R
Chief Engineer
Palomar-Engineers.com
PAPA System - September 2018
This presentation available on website
Copyright 2013-2018 Palomar Engineers, Inc.

---
Are you the SOURCE of RFI?
IT’S ALL YOUR FAULT WITH THAT BIG ANTENNA!

---
Are you a VICTIM of local RFI?
RFI Sources
Ham Antenna
Radiating Coax
Electronic Devices
Solar Systems
Grow Lights
HVAC motor
Plasma TV
DSL/Routers
Switching power Supplies
Washer/Dryer or other appliances
QRN - High Noise Floor – Weak Signals – NO DX – No fun!
HAM
Radio
Shack
RFI

---
What is RFI?
  - A radio frequency (>100 KHz) disturbance that causes an electrical circuit to function improperly Common Sources
    - Sunspots, Cosmic noise, Lightning, atmospheric static, AC power lines (no fix)
    - “Transmitters” -Ham, CB, AM/FM, electronic devices, speed controllers, inverters, switching power supplies, computer electronics, Cable/DSL/Ethernet (can use filters to fix)
  - Common Victims
    - Any electronic device that malfunctions by acting as an unintended “receiver” of RFI
How do you get RFI?

---
How RFI is Transferred
Source (antenna) and Victim (antenna) coupled via Path (all must be present to have RFI)
Multiple paths are very common:
Radiative - air
Conductive – wire(s)
Inductive - wire
Capacitive - wire
How to find the source & path

---
Typical RFI in your shack/home
TX Symptoms – caused by your transmitter or antenna
  - Hot microphone – RF lip burns, distorted audio
  - Antennas don’t tune correctly, high SWR, radiating coax
  - Your voice/transmission causes interference with consumer electronic devices acting as ham radio frequency “receivers” (e.g. computers, TV/audio system, security system, garage door opener, telephone, sprinkler systems, lights, etc.)
  - Wife Alarm goes off
RX Symptoms – caused by sources outside your radio
  - High receive noise level not due to atmospheric conditions
  - Birdies, chirps, buzzes, clicks, broadband noise on receiver
  - Distorted receiver audio
“Antennas” & paths

---
Typical RFI receiving “antennas"
AM broadcast, 160-80-60-40-30 meter RFI – long “antennas” - AC power lines, telephone/DSL lines, satellite/cable coax, long Ethernet cables, antenna feed line coax shield, antenna control/rotor cables, 2nd story ground wires (avoid ¼ wavelength ground wires)
FM broadcast, 20 meter-UHF transmitter RFI,– short “antennas” - speaker wires, device interconnect cables, mic cables, short Ethernet cables
“Antennas” pick up radiated or conducted RFI and a common mode current is induced on ALL unshielded antenna conductors from an RFI SOURCE
So how do we reduce this current?

---
Curing RFI Issues
I (RFI Current) = E (TX voltage)/R (Choking resistance)
Shut down the SOURCE (Set E to zero)
Choke the PATH (minimize E, increase R)
Protect the VICTIM(Set R very high)
Objective: Minimize RFI current, I
Trivia Q: Why is current abbreviated with I and not C?
Using ferrites to cure RFI

---
Ferrite Fundamentals
How to Select,
Buy,
Configure,
and Apply

---
Ferrite Topologies (Shapes)
Toroid or Ring
Snap On Bead
Slip On Bead
Fuzzy Ferret – not!
CHARACTERISTICS
Cheap, easy to install, suppress RFI from 100 KHz - 2 GHz
Work on all conductive paths (antenna feed line, AC/DC, I/O cables)
Lots of options in size, shape to suppress most RFI path currents
Are effective if you understand how ferrites work, how to choose the correct ferrite and where to install the ferrite for a particular RFI problem
Ferrite characteristics can be used to reduce RFI common mode current

---
Ferrite resistors add in series
More beads =
higher choking R (up to 30 MHz)
At 7 MHz:
5 beads = 400Ω
10 bead = 1000Ω
15 beads = 1600Ω
Impedance
Frequency 
Impedance (Z) = Resistance +/- Reactance

---
Ferrite resistors increase as (turns)2
If 1 turn = R, 2 turns = 4 x R, 3 turns = 9 x R
More R = less RFI wire current = less RFI radiated from wire or induced into wire. (I=E/R)
General rule: choking R > 10X line impedance
(e.g. > 500 Ω for 50 Ω cable but 5000 Ω is 10x better)
3 Turn
1 Turn
7 Turn
7 MHz:	100Ω	900Ω	2500Ω
Question: How do we choose the correct ferrite for the RFI frequency?

---
Ferrite Mix determines frequency range of effectiveness
Mix = chemical formula of the iron oxide with manganese-zinc (31, 75) or nickel-zinc (43, 61)
Select mix for max R at RFI fundamental frequency NOT frequency of receiver.
Example:
for .1-10 MHz use mix 75/77
for 1-300 MHz use mix 31
for 20-250 MHz use mix 43
for 200-2000 MHz use mix 61
Most popular ham frequency mixes are 31, 43, 61, 75, 77.
Wrong or unknown mix will probably not work so……. Know how to buy

---
How to buy Ferrites the right way!
=
BUY With CONFIDENCE!!
Product Labeling (Mix, Frequency, Impedance) + Known Vendor = Winner!
So let’s recap RFI 101

---
Ferrite Use Recap
Determine RFI interfering frequency & suspected Path
Choose proper mix (31, 43, 61, 75/77) to suppress RFI fundamental frequency
Choose Topology(slip, snap, ring) to fit the Path “Antenna”
Install ferrites – retest for RFI suppression
Consider additional ferrites or Paths if RFI persists
  1. Most popular Mix for HF is MIX 31 (1-300 MHz)
  1. (Mix 75/77 for .1-10 MHz, Mix 61 for 200-2000 MHz)
  1. How and where do you put the ferrite band aid for transmitter RFI?

---
Transmit RFI Solution
Tip #1 - Install Transceiver, Linear Amp RFI Filters
Goal: Minimize SOURCE RFI from radio and amplifier “antennas”

---
Transceiver/Amp RFI Kits
Palomar RFI kits for all brands of transceivers and amplifiers
Transceiver RFI Kit
Linear Amplifier RFI Kit
ICOM 7300
HEATHKIT SB220
Clean up the RFI SOURCE first – your radio and amp

---
Transmit RFI Solution
Tip #2. Stop Transmit RFI current on coax braid
ALL coax fed antennas need a feed line choke at the antenna feed point!!!!!
OR
Your dipole will become a tripole
Your unipole (vertical) will become a dipole

---
Typical Coax Fed Antenna System
Technical requirements for feed line choke selection

---
Choose choking resistance > 500Ω over frequency range used
Narrow Band
Wide ………….. Band 
Super Choker
1-10 MHz >2K
5KW PEP
1K-6K Z
3 pounds
Verticals
AM/RTTY Contesting
Line isolator
1-160 MHz >2K, 1.5KW PEP, 1K-6K ZΩ, 1 pound. All coax lines, Optional ground, static bleeder
DO NOT BUY CHOKES with NO SPECS!

---
Receive RFI Solution
Tip #3. Install Coax Noise Filter to Suppress RX RFI
Less common mode noise current (RFI) = More DX!
How to select and install filters for maximum effect

---
Receive RFI Problem
Symptoms: High noise levels, spurs, buzzes, periodic signals across bands
Typical Receive Chain Connections

---
Coax Feed Line Noise Filters
˃˃˃ One of the best kept secrets in ham radio!!! ˂˂˂
Placed at RADIO END of coax feed line to suppress common mode current on coax braid between antenna feed point choke and radio
Now AC/DC Filters

---
Receive RFI Solution
Tip #4. Install AC/DC Noise Filters
Lower Noise Floor = Higher SNR = More DX!
How to select and install filters for maximum effect
Goal is to reduce common mode RFI current superimposed on regular signal INTO “receiver”

---
RFI – AC/DC Line Chokes
1.4” ID
3” ID
1.4” ID
3” ID
1” ID
Choose mix frequency range and size to fit cable – use multiple turns
Wall Warts

---
Wall Wart RFI Noise Reduction Kit
Wall Wart switching DC power supplies that plug into the AC power line plug and provide DC power to laptops, routers, battery chargers, cell phone chargers, etc are a known source of broadband RFI
A simple ferrite ring filter on the DC power line can help suppress the RFI noise affecting the device or keep the DC power cord from acting as an antenna and radiating RFI from the powered device.
RFI Filter on DC Cord
Economy 10 ring kit

---
Transmit RFI Solution
Receive RFI Solution
Tip #5. Install Solution Specific RFI Kits
Our Goal: Minimize Transmit RFI to Home Electronics and Home Electronics RFI to receiver
Garage Door Opener RFI Kit
Washer/Dryer/Refrigerator RFI Kits
Home Alarm RFI Kit
Computer Desktop, laptop, router RFI Kits
Home Theater A/V Systems

---
Neighborhood RFI Solutions
Recommendation: Use RFI kits for specific problems, have neighbor purchase and install – do not make mods to neighbors equipment! MOST problems are RFI picked up by AC power/phone lines so ferrite filters work well.
Prize Time

---
Prize Question #1
What are 2 ways to increase the choking resistance of a ferrite filter choke?
Use high resistance wire and multiple turns on bead
Use multiple turns and double shield coax
Use multiple beads in series with multiple turns
Use mix 31 and mix 77 beads in series with a single turn

---
Prize Question #2
Mix 77 is used in which frequency range to suppress RFI common mode current?
A) 1-300 MHz
B) 200-2000 MHz
C) .1-10 MHz
D) 1-2000 MHz
E) CB Band Only

---
Prize Question #3
What is one of the best kept secrets in ham radio?
a)Ladder line has more loss than coax
b) A coax wound choke can cover all frequencies from 160-6 meters if the coax is long enough
c) All ferrites work on all frequencies, so buy the cheapest
d) Coax noise filters reduce common mode noise level in your receiver so you can hear more stations
e) All extra class hams go to heaven

---
Bonus Prize Question #4
Which company is your best source for RFI solutions?

---
Website: www.Palomar-Engineers.com
Email: Sales@Palomar-Engineers.com
Phone: 760-747-3343
Bob Brehm, AK6R – Chief Engineer
This presentation available on the website.